## Slide 1: Bootlegger
Sam Lobel
Yixing Du

## Slide 2: The feedback loop
Sensing on the insole
Processing on the computer
Actuation using a DC motor in the heel of the shoe

## Slide 3: Sensing
Sensing takes place in the sole
Soft potentiometers give COM readings along a given line
Record data through 5 ADC port
Data is sent from one mBed to another using two zigbee radios
To guarantee communication, we wrote a protocol sort of like the preamble one seen in class.

## Slide 4: Processing
The computer talks to the with serial communication
Every 30 seconds, breaks 8000 data points into around 10 steps
Compresses each step down to 16 features that each represent a different place your foot has been during a step
SVN analyzes this result against training data, where we purposely walked with supination, pronation, or normal gait.

## Slide 5: Actuation
Computer sends walking state back to the mBed, and then to the ankle through radio
Using switch transistors to get 5V logic, the mBed controls an H-Bridge motor hooked up to 4 9V batteries (2 series, two parallel).
Motor spins appropriately to pull on foot in a way that would correct stride.
Loop: closed.